## Slide 1: Thoughts on Agent Policy-aware Network
China Mobile
Xiaoqiu Zhang

## Slide 2
Flow-aware Agent-aware
QoS-based Policy-intent-based
Network-driven Agent-network collaboration
Background & Motivations
AI Agents are widely used in many industries and different from traditonal applications, raising new deamnds for network. Howerver, traditional network architectures can no longer meet the demand for efficient collaboration between Agents and networks.
Current network deliver differentiated quality of service guarantees primarily based on traditional QoS mechanisms, but fail to understand the intents and requirements of AI Agents.
Challenges：
Lack of intent expression
Insufficient collaborative decision-making
difficult to achieve end-to-end SLA assurance
Inflexible security mechanisms
Key Transformations:
Notes: Traditional applications can’t proactively decide how to use network services, and can only passively receive the service provided by network. By contrast, Agent is an autonomous intelligent entity capable of perceiving, making decisions, and executing tasks. Furthermore, it can even interact with networks to express policy intents and select different network service abilities.
3 And Traditional networks can’t match the dynamic, bursty needs of Agents.

## Slide 3
New Paradigm of "AI Agent Policy-Aware Network"
AI Agents need to act as network users and schedulers, better expressing their intents and requirements for network guarantees. It proactively perceives network quality, discovers network services, and guarantees service quality based on performance and cost, autonomously selecting corresponding network paths or egress nodes.
Networks need to identify, understand, and execute the intents and policies of AI Agents, enabling collaborative decision-making between Agents and networks, end-to-end SLA assurance, and secure transmission.
3. Agent Policy-aware SLA Level Assurance
4. Agent Policy-aware Secure Transmission
1. Agent Policy-aware Performance Measurement
2. Agent Policy-aware Path Optimization
Agent policy-aware controller
Service agent
APA Device
APA Device
Net agent
APA Device
APA Device
Global intent
Local intent
APA Netwrok
Complicate policy
Real-time policy
Cloud
APA ID
Network agent
E2E policy
Agent ID、Task ID
Notes: 是否policy ID 和现有得ARN/APN是什么关系 智能体是否需要做决策
APAD is in charge of fast local intent processing, policy execution and status monitoring – to achieve quick local responses. APAC undertakes global complex intent parsing, cross-domain resource coordination, policy optimization and closed-loop management – to realize overall global planning.

## Slide 4
Use case 1: Agent Policy-aware Performance Measurement
Service Agents have strict latency and jitter requirements for specific data flows (e.g., emergency rescue video streams), and need real-time end-to-end network quality perception to meet business SLAs.
Service agent
Network Measurement Agent
1.send structured measurement intents based on SLA requirements
APA Device/Path
2.select adaptive measurement protocols
3. collect performance data
4. receive structured measurement results
5. extract performance characteristics of business flows
6. predict traffic and security requirements based on datas, and map business semantic actions to traffic features
7. output explicit QOS requirement to netowrk（carrying Agent ID and task ID）
8. APAD generate APA ID and allocate dedicated network resouces
Notes: all without manual operation, forming an automated closed loop.

## Slide 5
Use case 2: Agent Policy-aware Path Optimization
When congestion or faults occur on the current transmission path, service SLAs may be degraded. The network should switch to a more optimal path without service interruption, enabling fault self-healing and experience self-optimization, thereby ensuring service continuity.
Service agent
APA Controller
(Path Optimization Agent)
APA Device/Path
1.2. receive network feedback of quality degradation alarms
1.1. perceive its own service experience degradation
2. send a request for path recalculation and switching
with service tolerance (e.g. lossless swtching)
3. calculates an optimal set of schedulable paths that meet constraints
4. confirm the switching strategy with service agent
6. execute seamless path migration
Schedulable Path Set Information Model:
Basic Identifier: Path ID / Path Group ID
Performance Attributes: Latency, jitter, packet loss, bandwidth, remaining bandwidth
O&M Attributes: Cost, priority, reliability, congestion probability
Constraint Attributes: Slicing support, cross-domain support, encryption support
5. select an optimal path from the path set
Notes: increased response time, request timeout

## Slide 6
Use case 3: Agent Policy-aware SLA Level Assurance
Different types of traffic from Agents feature high dynamism, burstiness and periodicity (e.g., scheduled big data synchronization). The network needs to allocate exclusive resources such as bandwidth on demand to realize "tidal scheduling" of network resources, greatly improve resource utilization, and ensure deterministic experience for critical services.
Service Agent
Resource Reservation Agent
APA Device/Path
1. predict future traffic trends and send "resource reservation intents" (including time window, bandwidth peak, and duration)
2. evaluates the global network load, and check whether the resources are sufficiant
3.3. negotiate a degradation strategy
3.1. provide the corresponding network slice /SRv6 policy, and complete the lifecycle management for current task
Yes
No
3.2. use the evolution of SFC to achieve the agent‘s ordered service

## Slide 7
Use case 4: Agent Policy-aware Security
For the sensitive data transmission in govenment, medical and financial scenarios, when Agents in different trust domains conduct data interaction, the network needs to dynamically match the corresponding security levels and encryption mechanisms to realize identity and context-based dynamic zero-trust security, ensuring that data only flows within authorized scopes.
Service Agent1
Security Agent
APA Device/Path
2. send "the required security intents"
2. parse, retrieve and match preconfigured cross-domain mutual trust policies
3. provides hierarchical security technologies on demand, including IPSec, QKD key distribution, and group secure transmission
4. The policies are automatically revoked after the session ends.
Service Agent2
1. exchange identity credentials and trust domain attributes
(e.g. national cryptographic algorithm encryption)

## Slide 8
Agent Policy-aware Network Solution Based on OpenClaw
System Architecture Design (Gateway-Node-Canvas)
Sensing Layer ——OpenClaw Nodes
Equipped with Network Sensor Skills to collect and upload real-time metrics such as latency, jitter, and packet loss
Decision Layer——OpenClaw Gateway
Aggregates data, Package network capabilities as standard OpenClaw Skills to be invoked by the strategy engine, and makes decisions via policy engines
Execution Layer——Invoking Network APIs
Invoke standardized network capability APIs to act on the actual environment and complete closed-loop optimization
Data Collection and Standardization：
Develop acquisition metrics and define a unified data format
Establish Basic Sensing and Feedback：
Enable the Agent to perceive network status and realize real-time reporting.
Achieve Closed-Loop Automation：
Complete the automation loop from sensing to execute for typical scenarios
Move To Predictive Collaboration：
Introduce ML/RL to evolve from reactive response to proactive prediction.
Key Implementation Paths

## Slide 9: Next Steps
Thank You!
Request more review and feedback to improve the draft.
Any comments are welcome.

## Slide 10
基于OpenClaw的智能体感知网络解决方案
感知-决策-执行闭环
持续感知网络状态，实时分析并执行最优调整策略。
端-边-云协同架构
边缘侧处理低延迟决策，云端负责复杂策略模型训练。
策略与通道解耦
网络调整策略与通信通道分离，支持灵活配置与扩展。
系统架构设计 (Gateway-Node-Canvas)
感知层 (OpenClaw Nodes) - 神经末梢
内置Network Sensor Skill，实时采集延迟、抖动、丢包等指标并上报。
决策层 (OpenClaw Gateway) - 智能大脑
聚合数据，通过策略引擎作出决策，调用工具库执行调整。
执行层 (外部环境) - 优化闭环
触发5G切片、QUIC协议优化或边缘节点切换，作用于实际网络环境。
关键实现路径
数据采集与标准化：开发插件采集指标，定义统一数据格式。
构建基础感知与反馈：实现Agent对网络状态的“看见”与实时汇报。
实现闭环自动优化：针对典型场景，完成从感知到行动的自动化闭环。
迈向预测性协同：引入机器学习，实现从被动响应到主动预测的进阶。
Notes: 大家好，本页将为大家介绍我们基于OpenClaw构建的智能体感知网络解决方案。我们的核心目标，是让每个智能体都具备“网络感知”能力，实现从被动响应到主动适应环境的飞跃。这背后有三大核心思想：首先是构建感知-决策-执行的完整闭环；其次是利用端-边-云协同来优化性能；最后是通过策略与通道的解耦来保证灵活性。
在系统架构上，我们充分利用了OpenClaw现有的三层架构。感知层由增强的OpenClaw Nodes组成，它们就像系统的神经末梢，负责采集网络数据。决策层是智能的OpenClaw Gateway，作为大脑，它分析数据并作出决策。最后，执行层将决策作用于外部网络环境，比如切换协议或申请5G切片，从而完成整个优化循环。
要实现这个方案，我们规划了四个关键步骤：从基础的数据采集开始，到构建感知反馈，再到实现自动优化闭环，最终迈向更智能的预测性协同。这是一个从无到有、从有到优的完整落地路径。