## Slide 1: Thoughts on Agent Policy-aware Network
China Mobile
Xiaoqiu Zhang

## Slide 2
Flow-aware Agent-aware
QoS-based Policy-intent-based
Network-driven Agent-network collaboration
Background & Motivations
AI Agents are widely used in many industries and different from traditonal applications, raising new demands for network. Howerver, traditional network architectures can no longer meet the demands for efficient collaboration between Agents and networks.
Current network deliver differentiated quality of service guarantees primarily based on traditional QoS mechanisms, but fail to understand the intents and requirements of AI Agents.
Challenges：
Lack of intent expression
Insufficient collaborative decision-making
difficult to achieve end-to-end SLA assurance
Inflexible security mechanisms
Key Transformations:
Notes: Traditional applications can’t proactively decide how to use network services, and can only passively receive the service provided by network. By contrast, Agent is an autonomous intelligent entity capable of perceiving, making decisions, and executing tasks. Furthermore, it can even interact with networks to express policy intents and select different network service abilities.
3 And Traditional networks can’t match the dynamic, bursty needs of Agents.

## Slide 3
New Paradigm of "AI Agent Policy-Aware Network"
AI Agents need to act as network users and schedulers, better expressing their intents and requirements for network guarantees. It proactively perceives network quality, discovers network services, and guarantees service quality based on performance and cost, autonomously selecting corresponding network paths or egress nodes.
Networks need to identify, understand, and execute the intents and policies of AI Agents, enabling collaborative decision-making between Agents and networks, end-to-end SLA assurance, and secure transmission.
3. Agent Policy-aware SLA Level Assurance
4. Agent Policy-aware Secure Transmission
1. Agent Policy-aware Performance Measurement
2. Agent Policy-aware Path Optimization
Agent policy-aware controller
Service agent
APA Device
APA Device
Net agent
APA Device
APA Device
Global intent
Local intent
APA Netwrok
Complicate policy
Real-time policy
Cloud
APA ID
Network agent
E2E policy
Agent ID、Task ID
Notes: 是否policy ID 和现有得ARN/APN是什么关系 智能体是否需要做决策
APAD is in charge of fast local intent processing, policy execution and status monitoring – to achieve quick local responses. APAC undertakes global complex intent parsing, cross-domain resource coordination, policy optimization and closed-loop management – to realize overall global planning.

## Slide 4
Use case 1: Agent Policy-aware Performance Measurement
Service Agents have strict latency and jitter requirements for specific data flows (e.g., emergency rescue video streams), and need real-time end-to-end network quality perception to meet business SLAs.
Service agent
Network Measurement Agent
1.send structured measurement intents based on SLA requirements
APA Device/Path
2.select adaptive measurement protocols
3. collect performance data
4. receive structured measurement results
5. extract performance characteristics of business flows
6. predict traffic and security requirements based on datas, and map business semantic actions to traffic features
7. output explicit QOS requirement to netowrk（carrying Agent ID and task ID）
8. APAD generate APA ID and allocate dedicated network resouces
Notes: all without manual operation, forming an automated closed loop.

## Slide 5
Use case 2: Agent Policy-aware Path Optimization
When congestion or faults occur on the current transmission path, service SLAs may be degraded. The network should switch to a more optimal path without service interruption, enabling fault self-healing and experience self-optimization, thereby ensuring service continuity.
Service agent
APA Controller
(Path Optimization Agent)
APA Device/Path
1.2. receive network feedback of quality degradation alarms
1.1. perceive its own service experience degradation
2. send a request for path recalculation and switching
with service tolerance (e.g. lossless swtching)
3. calculates an optimal set of schedulable paths that meet constraints
4. confirm the switching strategy with service agent
6. execute seamless path migration
Schedulable Path Set Information Model:
Basic Identifier: Path ID / Path Group ID
Performance Attributes: Latency, jitter, packet loss, bandwidth, remaining bandwidth
O&M Attributes: Cost, priority, reliability, congestion probability
Constraint Attributes: Slicing support, cross-domain support, encryption support
5. select an optimal path from the path set
Notes: increased response time, request timeout

## Slide 6
Use case 3: Agent Policy-aware SLA Level Assurance
Different types of traffic from Agents feature high dynamism, burstiness and periodicity (e.g., scheduled big data synchronization). The network needs to allocate exclusive resources such as bandwidth on demand to realize "tidal scheduling" of network resources, greatly improve resource utilization, and ensure deterministic experience for critical services.
Service Agent
Resource Reservation Agent
APA Device/Path
1. predict future traffic trends and send "resource reservation intents" (including time window, bandwidth peak, and duration)
2. evaluates the global network load, and check whether the resources are sufficiant
3.3. negotiate a degradation strategy
3.1. provide the corresponding network slice /SRv6 policy, and complete the lifecycle management for current task
Yes
No
3.2. use the evolution of SFC to achieve the agent’s ordered service

## Slide 7
Use case 4: Agent Policy-aware Security
For the sensitive data transmission in govenment, medical and financial scenarios, when Agents in different trust domains conduct data interaction, the network needs to dynamically match the corresponding security levels and encryption mechanisms to realize identity and context-based dynamic zero-trust security, ensuring that data only flows within authorized scopes.
Service Agent1
Security Agent
APA Device/Path
2. send "the required security intents"
2. parse, retrieve and match preconfigured cross-domain mutual trust policies
3. provides hierarchical security technologies on demand, including IPSec, QKD key distribution, and group secure transmission
4. The policies are automatically revoked after the session ends.
Service Agent2
1. exchange identity credentials and trust domain attributes
(e.g. national cryptographic algorithm encryption)

## Slide 8: Next Steps
Thank You!
Request more opinions and feedbacks to promote our work.
Any comments are welcome.